## Slide 1: Primjer upotrebe HPC resursa – Izračunavanja u dinamici fluida i hemijskim procesima
Sreten Lekic
Prirodno-matematicki fakultet
Univerzitet u Banjoj Luci

## Slide 2: Šta je CFD?
Priprema problema iz oblasti dinamike fluida za rješavanje pomoću računara
Dijeljenje oblasti računanja (radne površine, ili zapremine) na mrežu elementarnih površina, odnosno zapremina)
Zadavanje početnih i graničnih uslova i rješavanje parcijalnih diferencijalnih jednačina transportnih i termodinamičkih procesa metodom konačnih elemenata (površina i zapremina) numerički, postupkom iteracije
Obrada i vizualizacija rezultata u prostoru i vremenu

## Slide 3: Ograničenja i problemi CFD
Problemi CFD računanja na 32bit-nim platformama: zbog ograničenja u memorijskom adresiranju programi za dizajniranje 2D, a posebno 3D mreža, nisu u toku rada uzimali više od 1,5 GB memorije, odnosno do približno1,5 miliona ćelija.
CFD programi koji bi prihvatili mreže ove veličine sami su nakon uvođenja raznih fizičkih mehanizama i pretpostavki brzo zauzimali blizu 4 GB 32bit-no adresabilne memorije, što je bila i krajnja granica koja se nije mogla preći

## Slide 4: Načini prevazilaženja problema
Ograničenje veličine memorije samo djelimično se rješavao segmentacijom radne zapremine (površine)
Dijeljenje na oblasti sa periodičnim ponavljanjem, na aksijalno simetrične oblasti i slično smanjio je potrebnu memoriju, ali tako ponuđeni rezultati davali su “simetrično” ponavljana rješenja što je ponekad bilo daleko od realne situacije.

## Slide 5: Prednosti i ograničenja 64bit-nih platformi
Problem 64bit-nog adresiranja teoretski bi rješio problem memorije
U praksi, komercijalne višeprocesorske jedinice imaju do 8GB raspoložive RAM memorije koja prije računanja može biti na raspolaganju programu.

## Slide 6: Djelimično rješenje nedovoljne veličine RAM memorije
Particioniranje radne oblasti i dodjeljivanje manjih cjelina procesorima pojedinačno. Uslov, a i problem je da prije particioniranja program ne smije preći raspoloživu memoriju.
Nakon particioniranja u batch modu (StarCD i Fluent) rješavanje se predaje raspoloživom broju procesora.
Smanjena je i mogućnost da u toku jednog iterativnog koraka dođe do prevelikog zahtjeva za memorijom

## Slide 7: Problemi komercijalnog softvera
Dodatni financijski uslovi za podršku povećanom broju procesora
Zahtjev za stalnim obnavljanjem teko poskupljenih usluga

## Slide 8
Detaljni poluempirijski modeli sagorjevanja.
Karakteristike plamene zone I emisija gasova
Aktivnosti MFBL
CFD simulacije

## Slide 9: CILJEVI
CFD modelovanje i procesi gorenja
Analiza hemijskih reakcija u procesu sagorjevanja
Raspodjele pritisaka, brzina, temperatura i ostalih fizičkih veličina
Koncentracije i dinamika ulaznih sastojaka vazduha i goriva
Koncentracije i osobine emisije produkata sagorjevanja (CO,CO2, H2O, NOx i drugih)

## Slide 10: Kreiranje 3D mreže
Trodimenzionalna mreža isječka plašta gorionika koja formira oko 800 000 ćelija oblika tetraedra i omogućava rješavanje parcijalnih diferencijalnih jednačina transportnih i termodinamičkih procesa, te posebnih manifestacija dinamike fluida metodom konačnih zapremina

## Slide 11: Kreiranje 3D mreže
Mreže su kreirane u pretprocesorskim paketima StarCD Softvera - Prostar i Fluentovog Gambita, a zatim se prema mogućnostima 32bit-nih i 64bit-nih verzija ovih CFD broj ćelija povećava adaptacijama mreže u glavnom programu

## Slide 12: Stabilnost rješenja

## Slide 13
Raspodjela po brzinama u jednoj od poprečnih ravni plašta gorionika (StarCD)

## Slide 14
Prikaz raspodjele brzina u istoj ravni u u istom rezimu rada u Fluentu

## Slide 15
Temperaturna raspodjela u Fluentu

## Slide 17: Galerija rezultata

## Slide 18
Velocities distribution at the narrow segment of burner mantle

## Slide 19
Y =0.4694-2.24371 X-25367.73856 X\+
(2)+8.3427E6 X\+(3)+3.04111E8 X\+
(4)-2.3206E11 X\
+(5)+9.46953E12 X\+(6)+1.45424E15 X\+(7)-
1.15033E17 X\+(8)+1.95103E18 X\+(9)
Estimated a polynomial fitted curve for semi-empirical modeling of velocities distribution

## Slide 20
Mass fraction of NO at the narrow segment of burner mantle

## Slide 21
Estimated family of curves for further fitting and semi-empirical modeling of NO concentration

## Slide 22
Flux with average velocity about ms-1 and faster flux (2 ms-1) at figure below on next page give near values of power. Efficiency is falling down.

## Slide 24
Temperature distribution show the highest values above the holes of inner mantle

## Slide 25
Temperature of burner mantle segment at the end of burner (about 700 K) and at 40 kW power.

## Slide 26
Temperature of burner mantle segment at the end of burner (about 1000 K) and at 50 kW power.

## Slide 28
Strong stream of creating NO above the slits

## Slide 35: Pitanja?