## Slide 1: Applied CFD: Simulating the built environment and beyond Anina Šarkić Glumac Wind Engineering Group Instutute of Numerical Analisys and Design of Structures Faculty of Civil Engineering, University of Belgrade
EUROCC4SEE | 20.-22. 05. 25. | Belgrade, Serbia
EuroCC4SEE
Belgrade
20-22 May 2025

## Slide 2: Let Me Introduce Myself
Assistant Professor
Faculty of Civil Engineering
University of Belgrade
Research Scientist
University of Luxembourg
European Evaluator
H2020-MSCA-ITN & HORIZON-MSCA-DN
Doctoral Studies
Building Aerodynamics Laboratory
Ruhr-University Bochum
Magister & Dipl. Ing. Studies
Faculty of Civil Engineering
University of Belgrade
I'm a civil engineer with a background in wind-tunnel testing and CFD, applying these tools to real-world civil and environmental challenges — and recently expanding into data assimilation and machine learning to enhance simulation.
Karman vortex street, Heard Island, Wikipedia

## Slide 3: Let Me Introduce Myself
Current Research projects
SeaDream – HORIZON-MSCA-SE-2023 (Partner)
Sustainable Marine Energy and Ecosystem Resilience Advancement through Digital Technologies and Real- Time Crisis Management
ERIES – HORIZON-INFRA-2021 (PI of sub-project)
ERIES – FLOATINGSOLAR: Wind and wave effects on FLOATING SOLAR panels
Previous Research projects
DATA4WIND – H2020-MSCA-IF-2019 (PI)
DATA4WIND – FNR, 2020 (PI)
SEEFORM – DAAD (Partner), etc.
Industrial projects
Bridge on the river Sava, Serbia, consultant for Niemann&Partner
High bay structure of Jysk-Nordic, Denmark, consultant for Niemann&Partner, etc.

## Slide 4: Applied CFD in Built Environment
China,
Source: https://www.istockphoto.com/photo/china-shenzhen-skyscraper-gm969333552-264204925?searchscope=image%2Cfilm
Source: www.flickr.com - "JP Morgan Chase Damage" by AlphaTangoBravo / Adam Baker
Source: www.flickr.com - ”Roof Damage" by Beige Alert
WIND LOADS
BRIDGE AERODYNAMICS
Boston Logan Airport,
Source: www.propmodo.com/can-tech-help-commercial-d/yatt hotel, Katrina 2005
Environmental Eng.
Applications
Civil Engineering
Applications
WIND
HARVESTING
POLLUTION

## Slide 5: Core Challenges
Turbulent Flow & Geometric Complexity & Variability of Structures
Ozmen et al., Buld. & Envio., 2016
Blocken et al., J. Buil. Perf. Sim., 2010
Source: https://en.wikipedia.org/wiki/File:Civic_Center

## Slide 6: Core Challenges
Variability of Wind Direction

## Slide 7
Pros
Clarity and Consistency:
Structured procedure that engineers can follow, reducing ambiguity in the design process.
Safety and Reliability:
Ensures that structures meet minimum safety and performance requirements.
Standardization Across Projects
Legal and Professional Accountability
STANDARDS & CODES
Main Design Methods

## Slide 8
STANDARDS & CODES
Main Design Methods
Cons
Simplified Geometries Only The Eurocode primarily addresses basic, regular-shaped structures. It does not adequately cover complex geometries, such as curved façades, high-rise buildings with irregular shapes, etc.
Standard Terrain Categories The terrain exposure categories are overly simplistic and may not accurately represent urban environments with varying building densities, topography, or vegetation.
Limited Guidance on Local Effects Effects like channeling, vortex shedding, flutter and wake interactions are not well addressed.
https://greatnorthroad.co.uk/ferrybridge-power-station
Eurocode 1-4

## Slide 9
WIND TUNNEL
Stand alone tool!
Well-established, controlled and repeatable
Low spatial resolution of the measuring points
Scaling issues
EXPERIMENTAL
FIELD MEASUREMENTS
Real-world, high-fidelity data
Long-term monitoring
No scaling issues
Low spatial resolution of the measuring points
Difficult to control
Flexible & scalable
Captures detailed flow around complex geometries
Ideal for parametric studies
Sensitive to input (e.g. inflow) conditions
Needs validation!
NUMERICAL
CFD
Main Design Methods

## Slide 10
WIND TUNNEL
Where are we now?
CFD
Main Design Methods
VALIDATION
Well-established, controlled and repeatable
Low spatial resolution of the measuring points
Scaling issues
Flexible & scalable
Captures detailed flow around complex geometries
Ideal for parametric studies
Sensitive to input (e.g. inflow) conditions
Needs validation!

## Slide 11
WIND TUNNEL
CFD
Main Design Methods
VALIDATION
WIND LOADS
Each method plays a distinct role. WT & CFD used together, form a powerful tool for understanding and designing with wind.

## Slide 12
WIND TUNNEL
CFD
Main Design Methods
ENVIRONMENTAL STUDIES
VALIDATION

## Slide 13: How we handle turbulence numerically?
Approaching Flow - Atmospheric Boundary Layer (ABL)
Kostadinovic Vranesevic, University of Belgrade, 2025

## Slide 14: How we handle turbulence numerically?
Discretization of Navier-Stokes Equations
Number of cells: 10x106
Number of cells: 1,2x106

## Slide 15: Why such level of resolution?
Flow
Pressures/Forces
Complex flow

## Slide 16: Main QoI for Assessing the Wind Loads?
Pressure Coefficients & Forces
… Aeroelastic Forces
roof top
Flutter in Bridges
Loads on Structures

## Slide 17: Main QoI for Assessing the Environmental Engineering Studies?
Application Based
- Velocities & Turbulence Intensities
- Pollutant concentrations, etc.
China,
Source: https://www.istockphoto.com/photo/china-shenzhen-skyscraper-gm969333552-264204925?searchscope=image%2Cfilm
Wind Microclimate Assessment
and/or Optimisation
Pittsburgh,
Source: www.post-gazette.com/news/weather-news/2023/202303250072
Kublaj et al., JWEIA, 2024
Blocken et al., JWEIA, 2016
Pollution & Mitigation Studies

## Slide 18: How we handle turbulence numerically?
Reynolds-Averaged Navier–Stokes
RANS
Efficient estimates
Steady state or Ensemble Averaged
Lack of accuracy
Low fidelity simulation
High comp. costs
Transient response
Satisfactory accuracy
High fidelity simulation
Large Eddy Simulation
LES
How do we choose a CFD Approach?
Engineering Judgment & Experience
Wind Load Studies – prefer LES if feasible
Environmental Eng. Studies - RANS often sufficient

## Slide 19: Our Approach
Wind Tunnel

## Slide 20: Our Approach
Virtual Wind Tunnel
In case of LES:

## Slide 21: Our Approach
Virtual Wind Tunnel
ABL in case of LES:

## Slide 22: Our Approach
Virtual Wind Tunnel
Bridge Aerodynamics Specialized Experiments
Vortex Shedding
Torsional Divergency
Flutter, etc.

## Slide 23: High Rise building
Loads on the Roof Top
(scale 1:300)
roof top
Cp MEAN
Cp RMS
0
1
-3
0
Cp PEAK
-8
0
10%. 52.88%
20% 83.72%
30% 96.93%
Cp MEAN
Cp PEAK
LES Pressures -Roof Top
LES vs Exp

## Slide 24
External Pressure Coefficients – Designed Values
High Rise building
Whole Wind Rose!
→ for each direction
– one simulation!
-8
3

## Slide 25: Bridge Aerodynamics - Flutter
*) ploted values related to URANS results
Tacoma Narrows collapse 1940
Virtual WT vs Experiments

## Slide 26: Bridge Aerodynamics - Flutter
Aeroelastic Lift Force
One Simulation!

## Slide 27: HPC Usage – Absolute Necessity!
High – Rise Building Case
Pre-calculation - Course Mesh:
4,8x106 cells, 5575 CPUh
Main Calculation - Fine Mesh:
10x106 cells, 50000 CPUh
→ for only one wind direction!
Bridge Case
Pre-calculation - Course Mesh:
0,5x106 cells, 1300 CPUh
Main Calculation - Fine Mesh:
1,2x106 cells, 13440 CPUh
→ for only one moving mesh case!

## Slide 28: Next Steps… – Machine Learning, Data Assimilation…
How to predict the urban wind flow patterns accurately but with a reasonable computational cost?
How can we use previous knowledge in diverse urban landscape (application in optimisation studies)?
3 LES high-fidelity sim.
for 7 wind directions!
How can we use knowledge from experiments (or high-fidelity sim.) to speed-up and enhance the simulations?
Transfer Learning
Data Assimilation

## Slide 29: Wind Engineering Group
Faculty of Civil Engineering
University of Belgrade
Kristina
Kostadinović Vranešević
Miloš Jočković
Anina
Šarkić Glumac

## Slide 30: Thank you!
EUROCC4SEE | 20.-22. 05. 25. | Belgrade, Serbia
EuroCC4SEE
Belgrade
20-22 May 2025