## Slide 1: High-Performance Computing in Electromagnetics
Group for Electromagnetics, Antennas and Microwaves
School of Electrical Engineering, University of Belgrade
Presenter: Dragan Olcan, Professor (olcan@etf.bg.ac.rs)
Contributors: Prof. A. Djordjevic, Prof. B. Kolundzija, Prof. M. Ilic, Prof. M. Stevanovic, Assoc. Prof. Slobodan Savic, Assoc. Prof. Miodrag Tasic, Dr. Jovana Petrovic, Dr. Jelena Dinkic, MSc Darko Ninkovic and MSc Anja Kovacevic
EuroCC4SEE Workshop in Belgrade

## Slide 2: Electromagnetics in General
~150 years ago J.C. Maxwell A Treatise on Electricity and Magnetism
Equations rewritten by Oliver Heaviside
Computational model of all electric devices (on macroscopic level)
  Kirchhoff's circuit laws are a special case
Examples: light bulbs, mobile phones, microwave ovens, antennas, motors, computers, drones, radars, etc.
The microscopic level (light & semiconductors) included by quantum electrodynamics ~1950

## Slide 3: Computational Electromagnetics
Solving Maxwell’s equations analytically is possible only for very simple structures (integral and differential equations)
Computers made a revolution in EM about 70 years ago
Computational electromagnetics = using computers to design and analyze EM sources & fields
Linear EM system is transformed into a set of linear equations (MoM or FEM): solutions are coefficients in approximation of charges, currents or electromagnetic fields
Linear CEM problem = Integration + linear algebra @ full steam
  LAPACK library, https://www.netlib.org/lapack/
  INTEL Math Kernel Library (MKL), https://www.intel.com/content/www/us/en/developer/tools/oneapi/onemkl.html
  NVIDIA cuBLAS, CUDA , https://developer.nvidia.com/cublas
Solving nonlinear CEM problem = heuristics
PhD in CEM = EM + programming + high-performance computing

## Slide 4: Just as we speak in IEEE AP
Benchmarking CEM codes
  Accuracy and
  Speed
Standard
  EM Problems
  Computers

## Slide 5: Machine Precision in CEM (Conversion to Linear Equations)
Numerical solutions down to machine precision
64-bit yields max. 15 significant digits
Novel algorithms for numerical integration are developed
J. G. Perović, D. I. Olćan, B. M. Kolundžija and A. R. Djordjević, "A Singularity Cancelation Transformation for Entire-Domain Analysis of 2-D Structures With High-Precision Integration," IEEE Transactions on Antennas and Propagation, 2019, doi: 10.1109/TAP.2019.2891401

## Slide 6: High Accuracy: 24hrs on Desktop PC

## Slide 7: EM Parameters of Materials
Extraction of EM parameters of materials
Step 1: measurements
Step 2: accurate EM ~2 days of simulation
Step 3: extraction from steps 1 & 2
J. G. Petrović, D. I. Olćan, N. N. Obradović and A. R. Djordjević, "High-Precision Method of Moments Applied to Measurement of Dielectric Parameters at Microwave Frequencies,“ IEEE Transactions on Microwave Theory and Techniques, 2022, doi: 10.1109/TMTT.2021.313629

## Slide 8: Antenna Design Needs HPC!
IRA: Impulse radiating antenna
Design, prototype & measurements
2 weeks of design using HPC cluster: 48 CPUs+256 GB RAM + 4 GPUs
M. F. Miletić and D. I. Olćan, "Impulse Radiating Antenna With Six Feeding Arms and a Tapered Balun," IEEE Transactions on Antennas and Propagation, vol. 70, no. 8, pp. 6414-6422, 2022, doi: 10.1109/TAP.2022.3161572

## Slide 9: For every pixel: CEM+DFT=12hrs
Impulse excitation
Spherical wave
Impulse EM wave
Impulse EM wave
Impulse EM wave

## Slide 10: Microwave Imaging: Non-invasive Medical Diagnostics
3D Distorted Born iterative method for brain imaging (brain tumor detection)
7 head tissues are estimated in 20 iterations using coarser grid (60 minutes each) and additional 10 iterations using finer grid (105 minutes each)
Intel Core i7-9700 CPU @3 GHz 8 cores, whole analysis lasted about 37.5 hours
Child phantoms: about 5 hours of simulation time per phantom with 4 tissues on a computer with two Intel® Xeon® Gold 6342 CPU @2.80 GHz (96 threads in total) and 1024 GB of RAM.
EU Horizon 2020: EMERALD Grant agreement ID: 764479, DOI 10.3030/764479 http://www.msca-emerald.eu/
T. Singh, D. M. Ninkovic, B. M. Kolundzija and M. N. Stevanovic, "Smooth Polynomial Approach for Microwave Imaging in Sparse Processing Framework,“ IEEE Access, vol. 10, pp. 120616-120629, 2022, doi: 10.1109/ACCESS.2022.3217221

## Slide 11: AI-Assisted Identification of Monitors
Identifying monitor state & type based on emanated EM fields
Technique based on (MLP) neural networks
12 monitors measured: 30,000 frequency spectrums with 501 components each
Trained ANNs identify monitor with the accuracy of 99%!
Training of 100 ANNs lasted 19.5 hours using Intel Core i7-9700 CPU @3 GHz with 8 cores
D. M. Ninković and D. I. Olćan, "AI-Assisted Identification of State and Type of Flat-Panel Monitors in the Presence of EM Noise,“ IEEE Transactions on Electromagnetic Compatibility, 2024, doi: 10.1109/TEMC.2024.3370653

## Slide 12: Machine Learning and AI for Antenna Modeling
ML models to model highly nonlinear relations (EM output vs. parameters)
Large datasets (100 million) Yagi-Uda antennas for training: 2 weeks of run time @ Intel® Xeon® Gold 6342 CPU / 96threads 1TB of RAM
Z. Stanković, D. Olćan, N. Dončov and B. Kolundžija, "Consensus Deep Neural Networks for Antenna Design and Optimization,“ IEEE Transactions on Antennas and Propagation, 2022, doi: 10.1109/TAP.2021.3138220.

## Slide 13: Localization of Field Sources due to Instruction Execution in Processor
Finding executed instruction in a processor based on EM fields
Noninvasive technique for hardware & software inspections
Nonlinear inverse problem utilizing CEM + modern heuristics to solve
F. Werner, D. Chu, A. Djordjević, D. Olćan, M. Prvulovic and A. Zajić, "A Method for Efficient Localization of Magnetic Field Sources Excited by Execution of Instructions in a Processor,“ IEEE Transactions on Electromagnetic Compatibility, 2018, doi: 10.1109/TEMC.2017.2742501

## Slide 14: GPU Solver: Large Problems
Computer configuration
  Intel Xeon CPU E5-2660 v2 @2.2GHz (2 processors) + 256 GB of RAM
  4 SATA HDDS (~100MB/s RW speed)
  8 identical GPUs GeForce GTX 680
    GPUs are placed in the Cubix XPRM-G3-82A GPU Xpander
Acceleration for 10k to 100k problems
Simulation time for 100k to 140k problem

## Slide 15: Large Structure: Smart Reduction
Frigate warship, 117 m long and 12.6 m wide
  A monopole antenna is placed on top of a 24 m high comm. tower
  The frigate is around 100 λ long
Significant reduction in number of unknowns and simulation times
  Negligible discrepancies in the calculated radiation pattern
Number of unknowns | Memory [GB] | Sim. time CPU | Sim. time GPU
86 894 | 56.3 | 8.39 h | 1.12 h
64 147 | 30.7 | 3.88 h | 31 min
51 844 | 20 | 1.6 h | 11.4 min
40 125 | 12 | 45 min | 6.4 min
33 564 | 8.4 | 26.6 min | 4.7 min

## Slide 16: Amazon Cloud Server: RCS of Tank
Bistatic RCS at 1,801 directions (20.8 hrs)
Monostatic RCS at 70 directions (6.9 hrs)
Frequency of 3.6 GHz
Reduction of ref. frequency and total shadow
Matrix fill-in and output results - CPU
Matrix inversion - GPU
Amazon cloud server
CPU: Intel Xeon E5-2686 v4 @ 2.3 GHz (2 processors)
64 threads, RAM: 488 GB
HDD: 3 Hard disks, 1000 MB/s
GPU: 8 x Tesla V100

## Slide 17: GPU Cluster: Large Problems
Acceleration of all phases of an EM simulation
Arbitrary number of: CPU threads, GPUs, GPU cluster nodes
Matrix solve time for 100 – 140k unknowns: 3.7 minutes for 100k unknowns on 4 GPUs
Global hawk – Monostatic RCS (8.2 hours)
Unknowns: 546k f = 5 GHz
Wing span: 36 m (600 λ)
Cluster: 8 nodes x 2 GPUs each (GeForce GTX 680 GPU card)

## Slide 18: GPU Cluster: Solver Scalability
Helicopter with one microstrip patch antenna on the fuselage at 1.8 GHz
Efficiency: (achieved acc.)/(max acc.)
Matrix fill efficiency > 83%
Matrix factorization efficiency 79%
Overall simulation efficiency > 80%

## Slide 19: Optimizations (Heuristics) in Design
Running one CEM analysis is just a beginning
Design = multiple iterations in the design space (optimizations)
Modern heuristics for design space searches: GA, DE, PSO, NSGA, etc.
Transient non-linear circuit analysis with ~200 elements = 2GB of data on HDD
Optimal route for drilling holes in PCB 165 drilling holes: 165! = 5.4∙10295 paths to search
Running @ 200PFlops ~1.7 ∙10273 years of calculations!
Horizon Europe, NGI Zero Core: Open-Hardware for Electrostatic Discharge Testing (O-ESD) 2024-2025, https://o-esd.etf.bg.ac.rs

## Slide 20: Conclusions
High-performance computing is indispensable tool in computational electromagnetics
State-of-the-art research in EM (and electrical engineering) is entangled with high-performance computing
Changes in industry and academia: desktop computers used for preparing models but actual computations done at HPC installations
Challenges ahead:
  running existing CEM codes on emerging HPC hardware
  efficient implementation of CEM algorithms on HPC architectures
  managing HPC resources (technical + economics aspects)
    minimizing power consumptions
    capital expenditures (capex) & operational expenditures (opex)